## Slide 1: INTRODUCTION TO RING BLOWER
RING BLOWER IS ALSO KNOWN AS REGENERATIVE BLOWER, SIDE CHANNEL BLOWER, TURBINE BLOWER, RING COMPRESSOR, VACUUM BLOWER, VORTEX BLOWERS AND MANY MORE NAMES
---------------------------------------------------------------------------
RAICO ENGINEERS,MUMBAI-400059

## Slide 2: GENERAL INFORMATION
The Ring Blowers / Side Channel Blowers / Regenerative Blowers / Turbine Blowers/Vortex Blowers/Lateral blowers are suitable for all those applications requiring considerably higher pressure, than those which can be achieved using centrifugal fans.
These blowers are also used in all those applications requiring an operating vacuum higher than the one achievable by a fan, but not as to require the use of a vacuum pump.
The rotating parts are not in contact with the casing. There is, therefore, no friction during operation and thus no internal lubrication is necessary.

## Slide 3: WORKING PRINCIPLE OF RING BLOWER
Air is trapped between the impeller pockets of the rotating impeller and is then accelerated centrifugally.
The air stream is ducted by centrifugal force into the side channel blower.
It is then taken up by the impeller pockets and the air is re-directed back into the following pocket, where the process is repeated.
The air is accelerated and compressed in the impeller with each cycle. The more the blower is throttled, either at the inlet or discharge, the greater the number of impeller re-entries and hence in-creased compression.
One can compare the movement of an air molecules in the blower with a spring, the pitch of which becomes tighter the more the air is throttled.
When you measure the pressure at different points on the ring channel, you find that it rises constantly from inlet to outlet .
The side channel principle works as a vacuum pump when throttled on the suction side, and as a compressor when throttled on the pressure side.

## Slide 4: GENERAL CONSTRUCTION OF RING BLOWER
General construction of RING BLOWER is with direct motor driven balanced radial impeller, housed in close tolerance housing, supported by pregreased sealed bearings and sealed with shaft seal.
Mostly pressure die casted aluminum alloy impeller and housings are popular as they provide rugged yet light equipment.
Inlet and outlet ports are mostly threaded and provided with silencer.
Multiple stage units, come with multiple impellers, housed in multiple housings.
Normal speed of impeller is approx. 2900RPM.

## Slide 5: MAIN DESIGN FEATURES OF RING BLOWER
Higher pressure Ratio Rated for continuous duty
Low Noise Level
(65 db Normal, 85 db Max.) 110% Overload protection
Pulsation- Free Discharge 10% Voltage fluctuation tolerance
100% Oil-Free Air IP 54 Protection
Provided with inlet and outlet silencer/ filter Class F insulation
Cooler running, Double sealed
NSK (Japan) Bearings
Low temperature rise CE approved
Bearing are packed with High Dynamically balanced,No, Vibration, and therefore
Temperature Grease for longer life Complete Dynamic stability
Easy Installation in Vertical or Horizontal Pressure Die Casted Aluminum alloy
Position Body, Impeller & Rotor and
CNC machined close tolerance
For the best performance
Minimal & Simple Maintenance

## Slide 6: OPTIONAL ACCESSORIES AVAILABLE
SUCTION FILTER VACUUM FILTER
PRESSURE GAUGE VACUUM GAUGE
PRESSURE RELIEF VALVE VACUUM RELIEF VALVE
ON/OFF VALVE NON RETURN VALVE
HOSE NOZZLE HOSE CLIPS
ANTI VIBRATION ACCOUSTIC
MOUNTINGS ENCLOSURE

## Slide 7: MANY APPLICATIONS OF RING BLOWER
FOR LABELLING & DRYING OF BOTTLES AND CANS
TO AGITATE AND AERATE WATER IN STP PLANTS,SPA/WHIRLPOOL/ SWIMMING POOL/FISHING TANKS/AQUA CULTURE TANKS
FOR FURNACE FUEL BURNING
FOR AGITATION OF LIQUID BATH
FOR PNEUMATIC CONVEYING OF SOLIDS / LIQUIDS
TO VACUUM TRANSFER OF COMPONENTS / SHEETS DURING PRINTING FEED
FOR TRANSFER OF PAPER /SHEETS/COMPONENTS
FOR BLOWING AWAY DEBRIS /SUCKING AWAY DEBRIS
DURING PROCESSING/SEWING/KNITTING KEEPING YARN/ THREADS IN PLACE
FOR SORTING/COUNTING OF CARDS/ENVELOPES/PAPERS
TO PROVIDE AIR CUSHION TO HANDLE DELICATE MATERIAL LIKE EGGS / GLASS.
TO SUCK DEBRIS/GASES FROM CLEAN ROOMS/ENCLOSED TUNNELS/LABORATORIES
FOR WASTE DISPOSAL /SLURRY DE-CLOGGING IN WASTE
FOR AIR BEARING /AIR MATRESS
FOR MEDICAL / DENTAL SUCTION UNITS
FOR AIR SAMPLING/MONITORING EQUIPMENT
FOR CABLE PRESSURISASION
FOR PANEL PRESSURISASION
FOR LIQUID/SOLID DISPENSING
FOR PROVIDING AIR CURTAIN TO SENSORS/INSTRUMENTS/AREAS

## Slide 8: COMPARISON BETWEEN DIFFERENT DESIGNS OF BLOWERS

## Slide 9: TYPICAL EXPLODED VIEW OF SINGLE STAGE RING BLOWER

## Slide 10: NOTES
WE APRECIATE YOU, SPENDING TIME WITH US, THROUGH THIS PRESENTATION.
WE HOPE THE EXPERINCE HAS BEEN ENRICHING.
SHOULD YOU NEED FURTHER INFORMATION OR ASSISTANCE IN DECIDING CORRECT SOLUTION TO YOUR BLOWER NEEDS,
PLEASE FEEL FREE TO COMMUNICATE WITH US AT
raicoengineers@gmail.com
OR CALL US AT
+91-22-2832 0514
YOU CAN ALSO VISIT OUR WEBSITE AT
blowersandblowersindia.com
RAICO ENGINEERS,14 AF, NEW EMPIRE INDSTRIAL ESTATE,
KONDIVITA ROAD,J B NAGAR,MUMBAI-400059,INDIA.