## Slide 1: INTRODUCTION TO RING BLOWER FOR WASTE WATER PLANT
RING BLOWER IS ALSO KNOWN AS REGENERATIVE BLOWER, SIDE CHANNEL BLOWER, TURBINE BLOWER, RING COMPRESSOR, VACUUM BLOWER, VORTEX BLOWERS AND MANY MORE NAMES
---------------------------------------------------------------------------
RAICO ENGINEERS,MUMBAI-400059

## Slide 2: GENERAL INFORMATION
The Ring Blowers / Side Channel Blowers / Regenerative Blowers / Turbine Blowers/Vortex Blowers/Lateral blowers are suitable for all those applications requiring considerably higher pressure, than those which can be achieved using centrifugal fans.
These blowers are also used in all those applications requiring an operating vacuum higher than the one achievable by a fan, but not as to require the use of a vacuum pump.
The rotating parts are not in contact with the casing. There is, therefore, no friction during operation and thus no internal lubrication is necessary.

## Slide 3: WORKING PRINCIPLE OF RING BLOWER
Air is trapped between the impeller pockets of the rotating impeller and is then accelerated centrifugally.
The air stream is ducted by centrifugal force into the side channel blower.
It is then taken up by the impeller pockets and the air is re-directed back into the following pocket, where the process is repeated.
The air is accelerated and compressed in the impeller with each cycle. The more the blower is throttled, either at the inlet or discharge, the greater the number of impeller re-entries and hence in-creased compression.
One can compare the movement of an air molecules in the blower with a spring, the pitch of which becomes tighter the more the air is throttled.
When you measure the pressure at different points on the ring channel, you find that it rises constantly from inlet to outlet .
The side channel principle works as a vacuum pump when throttled on the suction side, and as a compressor when throttled on the pressure side.

## Slide 4: GENERAL CONSTRUCTION OF RING BLOWER
General construction of RING BLOWER is with direct motor driven balanced radial impeller, housed in close tolerance housing, supported by pregreased sealed bearings and sealed with shaft seal.
Mostly pressure die casted aluminum alloy impeller and housings are popular as they provide rugged yet light equipment.
Inlet and outlet ports are mostly threaded and provided with silencer.
Multiple stage units, come with multiple impellers, housed in multiple housings.
Normal speed of impeller is approx. 2900RPM.

## Slide 5: OPTIONAL ACCESSORIES AVAILABLE
SUCTION FILTER VACUUM FILTER
PRESSURE GAUGE VACUUM GAUGE
PRESSURE RELIEF VALVE VACUUM RELIEF VALVE
ON/OFF VALVE NON RETURN VALVE
HOSE NOZZLE HOSE CLIPS
ANTI VIBRATION ACCOUSTIC
MOUNTINGS ENCLOSURE

## Slide 6: COMPARISON BETWEEN DIFFERENT DESIGNS OF BLOWERS

## Slide 7: WHY RING BLOWERS FOR WASTE WATER PLANTS
Ring Blowers provide critical aeration for proper biological oxygen demand in water treatment applications.
Most other design blower applications can be satisfied by multi-stage or positive air-displacement blowers
and compressors, but at a relatively high price when factoring in their levels of energy consumption
and demanding maintenance requirements.
In contrast, RING BLOWER technology can serve as a practical, efficient and industry-friendly alternative to help keep costs down and output high.
Ring Blower Advantages
---Energy Efficiency.
----Very Silent compared to roots/lobe blower
---Developing pressures higher than required for applications, wastes energy. RING BLOWERS have been engineered to deliver the ideal pressure and flow for properly sized duty conditions at point of use.
---Low maintenance and high reliability. Fewer moving parts reduce wear, tear, maintenance and downtime to promote sustained blower reliability. Unlike competing technologies incorporating necessary sliding vanes, valves and pistons, the only contacting moving parts inside a RING BLOWER are two permanently sealed ball-bearing assemblies.
--- RING BLOWER supply clean air and are free of oil, excess moisture and other compressor-induced contaminants. They further eliminate any need for expensive, high-maintenance outlet filters and dryers or special water and oil traps.
---Direct drive. No need for V-belt or coupling drives.
---Permanently sealed motor bearings with 20,000- to 25,000-hour life eliminate the need for oil reserve levels and keep running whether with 8-hour-per-day or 24-hour continuous operation.
---Ring blower motors connected through VFD provides very easy control for achieving required flow at required pressure

## Slide 8: MAIN DESIGN FEATURES OF RING BLOWER
Higher pressure Ratio Rated for continuous duty
Low Noise Level
(65 db Normal, 85 db Max.) 110% Overload protection
Pulsation- Free Discharge 10% Voltage fluctuation tolerance
100% Oil-Free Air IP 54 Protection
Provided with inlet and outlet silencer/ filter Class F insulation
Cooler running, Double sealed
NSK (Japan) Bearings
Low temperature rise CE approved
Bearing are packed with High Dynamically balanced, No, Vibration, and therefore
Temperature Grease for longer life Complete Dynamic stability
Easy Installation in Vertical or Horizontal Pressure Die Casted Aluminum alloy
Position Body, Impeller & Rotor and
CNC machined close tolerance
For the best performance
Minimal & Simple Maintenance

## Slide 9: TYPICAL EXPLODED VIEW OF SINGLE STAGE RING BLOWER

## Slide 10: NOTES
WE APRECIATE YOU, SPENDING TIME WITH US, THROUGH THIS PRESENTATION.
WE HOPE THE EXPERINCE HAS BEEN ENRICHING.
SHOULD YOU NEED FURTHER INFORMATION OR ASSISTANCE IN DECIDING CORRECT SOLUTION TO YOUR BLOWER NEEDS,
PLEASE FEEL FREE TO COMMUNICATE WITH US AT
raicoengineers@gmail.com
OR CALL US AT
+91-22-2832 0514
YOU CAN ALSO VISIT OUR WEBSITE AT
blowersandblowersindia.com
RAICO ENGINEERS,14 AF, NEW EMPIRE INDSTRIAL ESTATE,
KONDIVITA ROAD,J B NAGAR,MUMBAI-400059,INDIA.